## Slide 1
Publishing Data to WIS2
Peter Mutai
Kenya Meteorological Service Authority
15th SEPTEMBER 2026

## Slide 2: Introduction
2
WIS2 is “data-agnostic”, it defines “the pipes through which data flows between WMO Members”
WIS2 supports data exchange for all WMO data disciplines: weather, climate, hydrology, …
WIS2 supports the WMO Unified Data policy and the Global Basic Observing Network (GBON)
However WIS2 is not limited to data governed by the WMO Unified Data Policy and GBON regulations …
WIS2-in-a-box can be used to publish any data on WIS2
this includes “recommended”-data, that may be access controlled

## Slide 3: The WMO Unified Data Policy
3
WMO Unified Data Policy describes two categories of data: core : data provided on a free and unrestricted basis recommended : data that has conditions on use defined by a license and which may be restricted using access controls Consult the WMO Unified Data Policy Cg-Ext(2021)/Doc. 4.1 to determine the relevant data policy for your data | 
WIS 2.0 | 
Global Cache
Global Broker
Global Discovery
Catalogue
MQTT
WIS2-node
“core”-data are downloaded and made available by Global Caches
“recommended”-data are to be downloaded directly from the data-provider
HTTP
download recommended data
download core data
access control

## Slide 4: GBON land-surface and upper-air
4
Global Basic Observing Network (GBON) represents core data:
Land-surface: every hour
Upper-air: twice daily
GBON defines a minimum number of stations to exchange data depending on country-size
more is better!
“exlore”-option on wis2box-homepage helps visualize your published data
As of wis2box-1.2, “explore” can be used for
../weather/surface-based-observation/synop (bufr2geojson must be enabled)
../weather/surface-based-observation/temp
visualization in wis2box is optional
Please refer to the WIGOS Data Quality Monitoring System for GBON compliance https://wdqms.wmo.int/

## Slide 5: GBON land and upper-air
5
wis2box dataset-editor provides templates to help publish data for land and upper-stations
Note: TEMP-data must be ingested in BUFR-format (no data-conversion available)
bufr2geojson should not be enabled for TEMP-data

## Slide 6: Publishing CAP on WIS2
wis2box dataset-editor provides a template to help publish CAP XML
The Common Alerting
Protocol (CAP) is an XML-based data format for exchanging public warnings and emergencies between different system
WMO CAP Composer can be configured to forward CAP XML for publication on WIS2

## Slide 7: Publishing DAYCLI on WIS2
Publish DAYCLI on WIS2 in support of climate services and flagship WMO publications !
DAYCLI is the WMO exchange format for daily climate observations, transmitted via WIS2
The scientific need for daily climate observations:
Monthly resolution CLIMAT messages lose the daily resolution required for monitoring extremes and calculating climate indices
SYNOP (and their BUFR equivalent) use aggregation periods inconsistent with national
climate reporting practices and undergo less QC, metadata is also often missing DAYCLI resolves this by
Complements monthly CLIMAT with daily resolution data (CLIMAT are still required)
Use of aggregation periods consistent with national climate reporting practices
Improved QC and analysis compared to SYNOP
Improved provision of metadata within the DAYCLI message
wis2box dataset-editor provides a template to help publish DAYCLI

## Slide 8: Aviation data on WIS2
The data provider is responsible for ensuring aviation data is shared per ICAO regulations
From the Guide to the WMO Information System, Volume II (WMO-No. 1061) section 2.8.1.1 :
“Meteorological data is an essential input for public weather services and aviation services alike. WIS2 provides the mechanism for data exchange in WMO. SWIM is the ICAO initiative to harmonize the provision of aeronautical, meteorological and flight information to support air traffic management (ATM). […]
During the WIS2 transition phase (2025–2033), meteorological data published via WIS2 will automatically be published to
GTS via the WIS2-to-GTS gateways.”
Aviation data on WIS2 is recommended and must have an appropriate license referring to ICAO
The wis2box-webapp will automatically set the data policy to recommended for datasets using aviation in the sub-discipline topic:

## Slide 9: Adding a license for recommended data in wis2box
A license URL can be provided by:
WCMP2 for a ‘recommended’-dataset shall include a link with rel=‘licence’
Dataset-editor in wis2box-webapp requires you to provide a license-URL when setting WMO Data Policy = ‘Recommended’
{
"rel": "license",
"href": "https://mywebsite.com/license/my_dataset.html",
"title": "License for this dataset",
"type": "text/html“
}
Additional object added in links-array of WCMP2 :
URL on your organization website
Public copyright license from Creative Commons
The wis2box-instance itself, using a file in wis2box-public
example text for aviation data license can be found in the recipe for publishing aviation data in the WIS2 cookbook

## Slide 10: Using a custom license hosted on wis2box
To use a custom license hosted by your wis2box-instance:
Upload the file the “wis2box-public”-bucket in MinIO
Use as the license-URL <WIS2XBOX_URL>/data/<filename>

## Slide 11: Recommended data in WIS 2.0: access control
WMO recommended data shall be downloaded directly
from the WIS2 Node, access can be open or restricted
Global Cache
Global Broker
WIS 2.0
Global Discovery
Catalogue
MQTT
WIS2 Node
download recommended data
access control

## Slide 12: access control in wis2box
Within wis2box datasets can be made restricted by adding a token using ‘wis2box auth’ commands:
To access a restricted dataset Data Consumers should include the token in the HTTP-request-headers:
Datasets published on origin/a/wis2/…/data/core/… should never be restricted
Datasets published on origin/a/wis2/…/data/recommended/… can be restricted
to limit data sharing to specific data consumers
wis2box auth add-token --metadata-id urn:wmo:md:mw-mw_met_centre:surface-weather-observations Secr3tT0ken1!
curl -H "Authorization: Bearer Secr3tT0ken1!" "<canonical-url>"
proxy via wis2box-auth
WIS2-in-a-box
HTTP-proxy
-H “Authorization: Bearer Secr3tT0ken1!”
incoming
public
storage
download recommended data
download recommended data
data-consumer-1 not allowed
data-consumer-2 allowed
1
2

## Slide 13: No WIS2 Topic available for your data ?
Submit a request on the GitHub repository by opening a new issue or sending an email to wis@wmo.int
The Task Team on WIS2 Metadata will discuss the options and consult with other experts as needed
The new topics will be included in the proposal for amendments to be approved through the WMO fast-track approval
procedure.
  Approval by Chair of SC-IMT  Review by National Focal Points on WIS Matters  Approval by P-INFCOM and P- WMO
  The procedure takes 3 months at a minimum and occurs 2x a year at a minimum
Publication and implementation
Announcements in the WIS2 Operational Newsletter
New topics made available 20 June 2026 (FT-2026-1):
atmospheric-composition advisories-warnings/sand-and-dust advisories-warnings/air-pollution advisories-warnings/fires
advisories-warnings/ozone-and-ultraviolet-radiation advisories-warnings/nuclear-fallout
advisories-warnings/volcanic-activity observations/aerosol-particles-and-clouds observations/atmospheric-processes-and-kinetics observations/emissions observations/gases/greenhouse-gases observations/gases/ozone observations/gases/reactive-gases
observations/radiation-latent-heat/ultraviolet-radiation observations/surface-flux-densities/precipitation-chemistry observations/surface-flux-densities/dry-deposition
weather
maritime-safety-information/warnings maritime-safety-information/forecasts
maritime-safety-information/sea-ice-information surface-based-observations/amdar
surface-based-observations/uas (Uncrewed aerial systems)
surface-based-observations/weather-radar surface-based-observations/vertical-profilers (…such as wind profilers, lidar, VAD radar etc.) surface-based-observations/gnss-iwv
More operational satellites and instruments, e.g.
space-based-observations/oceansat-3/ocm
hydrology
space-based-observations/soil
surface-based-observations/atmospheric/precipitation surface-based-observations/water-quantity/ice surface-based-observations/water-quantity/lake surface-based-observations/water-quantity/reservoir surface-based-observations/water-quantity/snow surface-based-observations/water-quantity/stream
subsurface-based-observations/water-quantity/groundwater subsurface-based-observations/water-quantity/soil

## Slide 14: wis2box data ingest workflow
incoming
public
wis2box-management
apply data-mappings create WIS2-notifications create WCMP2-records
listen to incoming-bucket
publish to public-bucket
National Sector
storage
Dataset driven workflow triggered when wis2box-management receives a notification from the storage service
data uploaded
wis2box-management matches incoming data with datasets based on file-path
data plugins are applied to transform s publish the data

## Slide 15: How to upload data to wis2box
8
incoming
public
storage
National Sector
Data can be uploaded to wis2box-incoming in different ways Optimal solution will depend on systems used in national sector
data uploaded
Manual upload methods:
Interfaces in wis2box-webapp: manual submission using FM-12 form
or manual file upload interface
Using MinIO UI: manually create path and upload data, useful for testing data-workflow
Automating data upload (recommended!):
Scripts: write code to upload data using MinIO client software
Using SFTP protocol: forward data to MinIO SFTP-endpoint
NOTE: when uploading data in wis2box-webapp, received data
does not go into the “wis2box-incoming” bucket
Received data is converted and output is stored in “wis2box-public” bucket directly

## Slide 16: BUFR ?
BUFR (Binary Universal Form for the Representation of meteorological data)
a flexible binary format
mainly used to encode in situ and satellite observations
How BUFR Works:
BUFR message consists of a header and a body containing data and metadata.
BUFR descriptors define how data is structured and encoded within a BUFR message
Compression for efficient storage to reduce transmission times.
BUFR Table System
BUFR descriptors are stored in BUFR Tables (Tables A, B, C, and D).
  Table B contains all element descriptors with their definitions.
  Table D defines combinations of descriptors into predefined sequences
BUFR tables are part of the WMO Manual on Codes:
https://library.wmo.int/idurl/4/35625 new version is released every six months

## Slide 17: BUFR tools in wis2box
wis2box data plugins use the BUFR tools to enable data transformation prior to publication
csv2bufr enables any system to prepare a data-extract without needing local BUFR conversion tools
synop2bufr enables direct publication of FM-12 synop reports from manual observers
bufr2bufr splits bulletins and ensure data has a valid WIGOS-station-identifier
WIS 2.0
Global Cache
National Segment
Field
Server, Cloud or Satellite
AWS data logger
External provider
Data collection and processing system
WIS2 in a box
Global Broker
Global Discovery
Catalogue
Manual observer
MQTT
Different data-formats uploaded from National Segment
BUFR-data published on WIS2
CSV
FM-12

## Slide 18: BUFR tools in wis2box
or
‘wis2box-api’ container is based on a Docker image containing ecCodes software library
… the container also includes several BUFR-conversion tools that work with ecCodes
wis2box-api
Request wis2box-api to use BUFR tools for transformation
wis2box-management Transform using 2bufr data plugin
BUFR tools used within wis2box-api available to be used standalone: https://github.com/World-Meteorological-Organization/csv2bufr https://github.com/World-Meteorological-Organization/synop2bufr https://github.com/World-Meteorological-Organization/bufr2geojson

## Slide 19: Station metadata used in transformation to BUFR
BUFR to BUFR (bufr2bufr):
Splits by bulletin and check WIGOS-station-ID in station-list for associated topic
If WIGOS-station-ID missing add it (by matching with traditional station identifier)
if the location or station elevation are missing in the input BUFR use values from station metadata
CSV to BUFR (csv2bufr):
Check WIGOS-station-ID in input data is in station-list for associated topic
For fixed land stations: check input-data-location is less than 1km from station metadata location
FM-12 to BUFR (synop2bufr):
Add the WIGOS-station-ID, derived by matching with traditional station identifier in FM-12 input
Add the latitude, longitude, altitude and barometer height above sea-level in the BUFR content

## Slide 20: wis2box data plugins: bufr2bufr
plugins:
bin:
plugin: wis2box.data.bufr4.ObservationDataBUFR notify: true
file-pattern: ‘^.*\.bin$’
bufr4:
plugin: wis2box.data.bufr2geojson.ObservationDataBUFR2GeoJSON file-pattern: ’ ^WIGOS_(\d-\d+-\d+-\w+)_.*\.bufr4$’
BUFR processing (extraction of subsets)
File containing one or more
BUFR subsets
bufr2geojson
GeoJSON
Station list
WIS 2.0
One or more BUFR files

## Slide 21: wis2box data plugins: csv2bufr
csv2bufr
Tabulated CSV data from
observing station, including location
mapping template
bufr2geojson
GeoJSON
plugins:
csv:
plugin: wis2box.data.csv2bufr.ObservationDataCSV2BUFR template: aws-template.json
notify: true
file-pattern: ‘^.*\.csv$'
bufr4:
plugin: wis2box.data.bufr2geojson.ObservationDataBUFR2GeoJSON
file-pattern: ’ ^WIGOS_(\d-\d+-\d+-\w+)_.*\.bufr4$’
Station list
WIS 2.0
One or more BUFR files

## Slide 22: CSV-to-BUFR introduction
or
wis2box contains a built-in data-plugin for “CSV data converted to BUFR”
-Enables ingesting data in CSV format while publishing WIS2 notifications containing BUFR data
-Uses a mapping template to map input columns to BUFR codes
csv2bufr-transformation is provided by the ‘csv2bufr’ module that can also be used outside of the wis2box https://github.com/wmo-im/csv2bufr

## Slide 23: CSV-to-BUFR key ingredients
BUFR Mapping Template
CSV file
BUFR file(s)
csv2bufr

## Slide 24: BUFR mapping template
Template: JSON file defining mapping between columns in the input CSV data to codes encoded in the output BUFR data
… using the human-readable eccodes_key rather than the 6 digit BUFR FXXYYY code
"data": [
….
{"eccodes_key": "#1#nonCoordinatePressure", "value": "data:station_pressure", "valid_min": "const:50000", "valid_max": "const:150000"},
{"eccodes_key": "#1#pressureReducedToMeanSeaLevel", "value": "data:msl_pressure", "valid_min": "const:50000", "valid_max": "const:150000"},
{"eccodes_key": "#1#nonCoordinateGeopotentialHeight", "value": "data:geopotential_height", "valid_min": "const:-1000", "valid_max": "const:130071"},
{"eccodes_key": "#1#heightOfSensorAboveLocalGroundOrDeckOfMarinePlatform", "value": "data:thermometer_height", "valid_min": "const:0", "valid_max": "const:655.35"},
{"eccodes_key": "#1#airTemperature", "value": "data:air_temperature", "valid_min": "const:193.15", "valid_max": "const:333.15"},
... ]
BUFR Mapping template
Data CSV file
csv2bufr
BUFR file(s)

## Slide 25: BUFR mapping template
BUFR Mapping template
csv2bufr
Data CSV file
air_temperature
value=29.5
WARNING: Value (29.5) out of valid range (193.15 - 333.15); Element set to missing
valid_min: Minimum tolerable value valid_max: Maximum tolerable value
csv2bufr uses 'valid_min' and 'valid_max' to catch input errors: invalid values will not be encoded in the BUFR
"data": [
….
{"eccodes_key": "#1#nonCoordinatePressure", "value": "data:station_pressure", "valid_min": "const:50000", "valid_max": "const:150000"},
{"eccodes_key": "#1#pressureReducedToMeanSeaLevel", "value": "data:msl_pressure", "valid_min": "const:50000", "valid_max": "const:150000"},
{"eccodes_key": "#1#nonCoordinateGeopotentialHeight", "value": "data:geopotential_height", "valid_min": "const:-1000", "valid_max": "const:130071"},
{"eccodes_key": "#1#heightOfSensorAboveLocalGroundOrDeckOfMarinePlatform", "value": "data:thermometer_height", "valid_min": "const:0", "valid_max": "const:655.35"},
{"eccodes_key": "#1#airTemperature", "value": "data:air_temperature", "valid_min": "const:193.15", "valid_max": "const:333.15"},
... ]
BUFR file(s)

## Slide 26: The AWS template
AWS Template:
Standardized CSV format to ingest data from Automatic Weather Stations in support of GBON reporting
requirements
The format is intended for use with automatic weather stations reporting a minimum number of parameters, including pressure, air temperature and humidity, wind speed and direction and precipitation
Based on SI units, with no unit prefixes, e.g. Pa rather than hPa, Kelvin rather than degrees Celsius etc
Template = AWS in the Plugin Configuration refers to the ‘aws-template.json’ as defined in https://github.com/wmo-im/csv2bufr-templates

## Slide 27: The DAYCLI template
DAYCLI Template:
Standardized CSV format for converting daily climate data to BUFR sequence 307075
The format is intended for use with Climate Data Management Systems to publish data on WIS2
Requirement for daily climate observations to monitor extremes Daily observations of:
Minimum, maximum and average temperature over 24 hours period
Total accumulated precipitation over 24 hours period
Total snow depth at time of observation
Depth of fresh snow over 24 hours period
Recognition of different reporting practices by Members, explicit reporting of 24 hours period used
Additional metadata: method of calculating average temperature; sensor and station heights; exposure and measurement quality classification
Template = AWS in the Plugin Configuration refers to the ‘daycli-template.json’ as defined in https://github.com/wmo-im/csv2bufr-templates

## Slide 28: wis2box data plugins: synop2bufr
WIS 2.0
plugins:
txt:
plugin: wis2box.data.synop2bufr.ObservationDataSYNOP2BUFR notify: true
file-pattern: ‘^*_(\d{4})(\d{2}).*\.txt$' bufr4:
plugin: wis2box.data.bufr2geojson.ObservationDataBUFR2GeoJSON
file-pattern: ’ ^WIGOS_(\d-\d+-\d+-\w+)_.*\.bufr4$’
synop2bufr
File containing SYNOP messages (FM-12)
Station list
bufr2geojson
GeoJSON
One or more BUFR files

## Slide 29: SYNOP-to-BUFR
Station list CSV file
SYNOP FM-12 text file
BUFR file(s)
synop2bufr
pymetdecoder
pymetdecoder
https://github.com/antarctica/pymetdecoder
UK Research and Innovation (UKRI), 2021, British Antarctic Survey
csv2bufr
synop2bufr
https://github.com/wmo-im/synop2bufr
csv2bufr
https://github.com/wmo-im/csv2bufr

## Slide 30: SYNOP-to-BUFR
FM-12 SYNOP reports
Station list metadata
AAXX = data from fixed
land station
YY = 21 of the month
GG = 12 hour of observation
iw = 1 Wind speed obtained from anemometer in m/s
TSI
TSI

## Slide 31: wis2box data plugins: Common Alerting Protocol (CAP)
plugins:
xml:
- plugin: wis2box.data.cap_message.CAPMessageData notify: true
buckets:
- ${WIS2BOX_STORAGE_INCOMING}
file-pattern: ‘^.*\.xml$'
Validate against CAP v1.2 schema and verify digital signature
extract data-timestamp from content
CAP
WIS 2.0
CAP

## Slide 32: Publishing CAP on WIS2
25
wis2box dataset-editor provides a template to help publish CAP XML
The Common Alerting
Protocol (CAP) is an XML-based data format for exchanging public warnings and emergencies between different system
WMO CAP Composer can be configured to forward CAP XML for publication on WIS2

## Slide 33: Summary
WIS2 is a framework for sharing data for all WMO domains and disciplines
WMO Unified Data Policy provides guidance if data should be exchanged as “core” or “recommended”
Recommended data in WIS2 MUST include a license URL in the metadata record wis2box-instance can host the license-file if required
Recommended data in WIS2 MAY be access controlled
wis2box provides the option to add access-control using an authentication token
WIS2 is “data-agnostic”, please refer to WIGOS manuals for complete data requirements
wis2box provides additional tools to help support WMO international data exchange that are not part of the WIS2 regulations
(data-visualization, BUFR-conversion, CAP-validation, mapping-template for DAYCLI)
wis2box can publish any data on WIS2
Using predefined templates in the dataset-editor, or use template=other and “Universal Data”-plugin

## Slide 34: Summary
33
To publish data using wis2box you must first define a dataset and publish WCMP2
In wis2box, datasets are used to define both the discovery metadata and the data plugins Data plugins determine the actions taken to transform and publish the data
wis2box includes pre-defined data plugins to enable users to transform data to BUFR using ecCodes
The dataset-editor makes it easier for users to define the correct data-plugin for their data-type by providing “templates” that can be selected when creating a dataset
incoming
public
wis2box-management
apply data-mappings create WIS2-notifications create WCMP2-records
storage
National Sector
data uploaded
wis2box-management container listens to events from MinIO to trigger data processing The file-path of the incoming data is used to determine the corresponding dataset

## Slide 35
Thank You